## 1 Loading data into R
The data recorded from 4 electrodes result from a preprocessing briefly described in the main text and are stored as signed integer coded on 4 Bytes. They must be mutiplied by 0.12715626 on channels 1 and 4 and by 0.01271439 on channels 2 and 3 to get voltage in µV. They are sampled at 500 Hz and 600 second are stored. We can then read the data and assign them to variable Data_raw of our work space:

<<load-data>>=
reposName <- "http://www.biomedicale.univ-paris5.fr/physcerv/C_Pouzat/Data_folder/"
dN <- paste("SpinalCordMouseEmbryo_CH",1:4,".dat",sep="")
fullN <- paste(reposName,dN,sep="")
nSamples <- 500 * 600
Data_raw <- sapply(fullN, readBin, n=nSamples, what="integer")
Data_raw <- t(t(Data_raw)*c(0.12715626,0.01271439,0.01271439,0.12715626))
@
For readers unfamiliar with R, the assignment operator “<-” can be replaced by the usual symbol “=”. R users can always get the documentation of native and user contributed functions with:

<<get-doc-on-readBin, eval=FALSE>>=
?readBin
@

The time derivatives of the measurements are simply obtained using a difference equation whose precision is o { \( δ^2 \)} :
f^′ { \( x \)} ={f { \( {x + δ} \)} - f { \( {x - δ} \)}} over {2 "" δ}
<<Data_derivative>>=
Data_derivative <- apply(Data_raw,2, function(x) c(0,diff(x,2)/2,0)*500/1000)
@
Here the unit of Data_derivative is µV/ms.
## 2 LFP detection
We are going to detect minima on each channel whose amplitudes are below a user set multiple of the channel standard deviation. We start by computing this quantity for each of the two versions of the data we might choose to work with, “raw” of “derivative”:

<<SD>>=
SD_raw <- apply(Data_raw, 2, sd)
SD_derivative <- apply(Data_derivative, 2, sd)
@

Here SD_raw and SD_derivative are vectors with as many elements as Data_raw and Data_derivative have columns, that is, as many elements as recording channels.
We are going to use a threshold of 4 times the standard deviation on each channel:

<<threshold-on-derivative>>=
factor <- 4
@
A inquiring reader could easily make another choice like using a threshold of 3.5:

<<threshold-on-raw, eval=FALSE>>=
factor <- 3.5
@

As explained in the main text we decided to identify events as minima exceeding (in absolute value) a threshold on 3 channels simultaneously. To this end we define a variable, activeElecNumber, which contains our number of required active channels. The value of this variable can easily be changed:

<<activeElecNumber>>=
activeElecNumber <- 3
@

The detection can now proceed:

<<detect-LFPs>>=
Times <- (1:dim(Data_derivative)[1])/500
timeLFP <- Times[apply(t(t(Data_derivative)/SD_derivative) < -factor,1,sum) >= 3]
@

We decide moreover to keep only detected events which are more than 100 ms apart. When “too close” events are found, the second one is discarded. This elimination is done recursively starting with the second event:

<<keep-far-apart-events>>=
timeLFP2 <- timeLFP
nbLFP <- length(timeLFP)
last <- 1; new <- 2
while (new <= nbLFP) {
  tDiff <- timeLFP[new]-timeLFP2[last]
  if (tDiff >= 0.1) {
    last <- last+1
    timeLFP2[last] <- timeLFP[new]
  }
  new <- new+1
}
timeLFP <- timeLFP2[1:last]
rm(timeLFP2)
@

We can now produce our summary Fig. 1 with:

<<make-figure,eval=FALSE>>=
Data_derivativeN <- Data_derivative/diff(range(Data_derivative))
Data_derivativeN.min <- min(Data_derivativeN)
Data_derivativeN <- Data_derivativeN - Data_derivativeN.min
Data_derivativeN <- t(t(Data_derivativeN)-c(0,1,2,3))
thresh <- -factor*SD_derivative/diff(range(Data_derivative)) - Data_derivativeN.min - c(0,1,2,3)
lwr <- 0-Data_derivativeN.min - c(0,1,2,3)
upr <- 2/diff(range(Data_derivative)) - Data_derivativeN.min - c(0,1,2,3)
plot(0,0,type="n",xlab="Time (s)",ylab="",xlim=c(0,600),ylim=c(-3,1),axes=FALSE)
sapply(1:4, function(i) lines(Times,Data_derivativeN[,i],lwd=0.2))
sapply(1:4,function(i) text(550,2-i,paste("Channel",i)))
abline(h=thresh,col="red",lty=2)
axis(1,at=(0:6)*100)
rug(timeLFP,col="red")
segments(-5,lwr,-5,upr,lwd=2)
@

<<fig=TRUE, echo=FALSE, results=hide>>=
<<make-figure>>
odfFigureCaption("Detection of LFP activity on the first time-derivative of the data. The same scale applies to all channels (vertical bar: 200 µV/ms). Channel specific detection threshold shown in dashed red. Detected events are shown as vertical red bar at bottom.",label = 'Figure' )
@